## Slide 1: Modularity and Comparisons
Christopher Mar

## Slide 2: Pseudo Operations
Similar to macros
Instructions that can are assembled as one or more native instructions

## Slide 3: Pseudo Operations
One reason to have pseudo-ops is that PLP instructions have fixed length of 32-bits
  Load immediate (li) requires more than 32-bits of information
    Composed of 2 I-type: lui and ori

## Slide 4: Pseudo Operations
Another reason is to make instructions more readable
    move $t2, $t1
      Copies a value from $t1 into $t2
      Assembles into the single instructions:
        addu $t2, $0, $t1

## Slide 5: Stack
Stack pointer register: $sp
2 pseudo-ops
  Push
  Pop

## Slide 6: Stack
Stack grows upwards in memory (address gets smaller) and starts at the largest memory address used by the stack
Initialization:
  li $sp, 0x10FFFFFC
Notes:   0x10FFFFFC is the largest memory address mapped to RAM

## Slide 7: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000000
0x10FFFFFC | 0x00000000
$sp
li $sp, 0x10FFFFFC
li $t1, 0x59

## Slide 8: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000000
0x10FFFFFC | 0x00000000
$sp
push $t1

## Slide 9: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000000
0x10FFFFFC | 0x00000059
push $t1
$t1
Copied
$sp

## Slide 10: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000000
0x10FFFFFC | 0x00000059
$sp
push $t1
$t1
Copied
Notes: Decrements $sp

## Slide 11: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000000
0x10FFFFFC | 0x00000059
push $t1 # Second push operation
$sp

## Slide 12: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
push $t1 # Second push operation
$sp
Copied
$t1

## Slide 13: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
push $t1 # Second push operation
Copied
$t1
Notes: Decrements c$sp

## Slide 14: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
pop $t2
$sp

## Slide 15: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
pop $t2
Notes: Increments $sp

## Slide 16: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
pop $t2
$t2
Copied

## Slide 17: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
pop $t3 # Second pop operation
$sp

## Slide 18: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
pop $t3 # Second pop operation
$sp
Notes: Increments $sp

## Slide 19: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
pop $t3 # Second pop operation
$t3
Copied

## Slide 20: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
Notice that even though things have been popped, they are still in memory

## Slide 21: Stack Underflow
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
An additional pop from the stack in this state will result in a stack underflow

## Slide 22: Stack Underflow Error
Attempts to read from memory address 0x11000000
  0x11000000 = 0x10FFFFFC + 0x4

## Slide 23: Stack Overflow
Occurs when attempting to push a value onto a stack that is already full

## Slide 24: Uninitialized Stack Pointer
If you forget to initialize $sp to a memory address pushing a second value onto the stack will cause a write error
  The first push will write to the address zero
  The second push will be at 0xFFFFFFFC
    0xFFFFFFFC = 0x0 – 0x4

## Slide 25: Jump-And-Link
jal label
  Performs a jump to label just like j instruction
  Stores address of next instruction in register $ra
    Return address

## Slide 26: Jump Register
jr $ra
  Performs a jump j to the address stored in $ra
  Typically used to return to where jal jumped from

## Slide 27: Example Program Demo Available in Video Lecture

## Slide 28: Subroutines and Functions
Subroutines perform a set of instructions
A function is like a subroutine, but it has context
  Context specific registers and a return address

## Slide 29: Context Switching
The current value of registers that are part of the function’s context are saved on the stack
  Upon returning the are restored to their previous value
  Referred to as a context switch

## Slide 30: Saved and Restored Registers
$a0 - $a3: Argument registers
$s0 - $s7: Saved registers
$t0 - $t9: Temporary registers (not saved by MIPS)
$ra: return address

## Slide 31: Function Return Value
$v0 and $v1 are used to hold return values from a function
  Not saved during function call or restored during return

## Slide 32: Call Pseudo-Op
call label
  Saves current registers to stack
  Performs a jump-and-link to label
  NOTE: the stack pointer must be initialized in order to use call without receiving an error

## Slide 33: Return Pseudo-Op
return
  Jumps to the return address
  Restores registers from stack

## Slide 34: Call and Return Usage
Call can directly replace all jal instructions to a specific label
  A return should replace the jr at the end of the function
Both call and return include the a nop as their last native instruction so they use up their own branch delay slots

## Slide 35: Call Stack
CPU Registers
Stack (RAM)
Inside main()
Function, foo(), is called
main values

## Slide 36: Call Stack
CPU Registers
Stack (RAM)
Inside foo()
Function, bar(), is called
main values
foo values

## Slide 37: Call Stack
CPU Registers
Stack (RAM)
Inside bar()
Function, snafu(), is called
main values
foo values
bar values

## Slide 38: Call Stack
CPU Registers
Stack (RAM)
Inside snafu()
Return to bar()
main values
foo values
bar values

## Slide 39: Call Stack
CPU Registers
Stack (RAM)
Inside bar()
Return to foo()
main values
foo values

## Slide 40: Call Stack
CPU Registers
Stack (RAM)
Inside foo()
Return to main()
main values

## Slide 41: Performance Tradeoff
Call is composed of 26 native instructions
  A combination jal and push pseudo-ops will be more efficient at saving fewer than13 registers
    Push pseudo-ops use 2 instructions each
  Option of using individual lw/sw with the $sp and a single $sp increment/decrement
Notes: Registers to be saved and restored needs to include $ra for nested

## Slide 42: Value Comparison (Inequality)
slt $t3, $t1, $t2
  If $t1 < $t2 then $t3 set to 1 (true)
    Else $t3 set to 0 (false)
  Result often used in a branch (compared with zero register)
    bne $t3, $0, was_less_than

## Slide 43: Inequalities
Inequality | Instruction | R if inequality is true
A < B | slt R, A, B | 1
A >= B | slt R, A, B | 0
A > B | slt R, B, A | 1
A <= B | slt R, B, A | 0

## Slide 44: Breakpoints
While in simulation mode, double-clicking to the right of a line number with an instruction adds a breakpoint

## Slide 45: Project 3 Pre Quiz and Demonstration